## Slide 1: Supporting Biomass electricity
In the Renewables Obligation (scotland)
20 December
Scottish Government & Forestry Commission Scotland
2011

## Slide 2: Overview of Report
Scope of Work
  To consider what is the best use of wood fibre given the opportunities both for renewable energy generation and the production of timber products from the conventional wood using industries;
  To consider the circumstances when it might be appropriate to use wood fibre for electricity generation, and at what scale.
In conducting this work XE has reviewed related Scottish and UK policy and background research. Relevant factors considered include:
  The Scottish Government’s renewable energy targets, and related policy aspirations set out in its Renewable Heat Action Plan and its Draft Electricity Generation Policy Statement and Route Map;
  UK Government policy including on the RO, EMR and the RHI;
  UK Committee on Climate Change analysis
  The perspectives of the forestry industries and wider bioenergy sector, with particular emphasis on the most recent work of the Wood Fuel Taskforce Report;
  Questions relating to woodfuel availability and use, and whether concerns about undue pressures on national woodfuel supply chains are also being found at a regional or local level.

## Slide 3: Scottish Government RO Consultation
As part of the RO Banding Review Consultation the Scottish Government is asking for views on:
  Removing support for large scale dedicated electricity stations;
  Establishing whether a capacity threshold should be set for small scale electricity only plants;
  Whether to mirror UK incentives for enhanced co-firing and conversion;
  Whether a maximum threshold for biomass CHP plants is required.

## Slide 4: Proposed RO Support levels
 | Scotland RO Banding Proposals |  | England & Wales (UK Govt) Banding Proposals | 
Renewable electricity technologies | Current support, ROCs/MWh | Proposed ROC support/MWh | Current support, ROCs/MWh | Proposed ROC support/MWh
Biomass conversion | No current band but eligible to claim 1.5ROCs under current banding arrangements | 1 Call for evidence | No current band but eligible to claim 1.5ROCs under current banding arrangements | 1 Call for evidence
Co-firing of biomass | 0.5 | 0.5 | 0.5 | 0.5
Co-firing of biomass (enhanced) | No current band but 0.5 ROCs under current banding arrangements | 1 Call for evidence | No current band but 0.5 ROCs under current banding arrangements | 1 Call for evidence
Co-firing of biomass with CHP | 1 | 1 | 1 | 1
Dedicated biomass | 1.5 | 1.5 | 1.5 | 1.5 to 31 March 2016 1.4 from 1 April 2016
Dedicated biomass with CHP | 2 | 2 in 2013/14 and 2014/15; 1.9 in 2015/16 and 1.8 in 2016/17 | 2 | 2 in 2013/14 and 2014/15

## Slide 5: UK Government RO Consultation
UK Government support for biomass electricity generation will be alongside support for use of biomass to meet renewable heat targets.
UK Government priority between 2013-17 is on “cheaper and more transitional technologies of conversion and co-firing”.
This is a priority because these “new biomass electricity bands will enable us to provide appropriate support for the use of existing infrastructure. Although existing plants may use biomass feedstocks less efficiently than new power stations, this policy offers reduced costs and reduces the risk of locking in long-term feedstock demand.”
A dedicated biomass RO level is proposed. Background analysis by Arup/Pöyry suggest that this will only incentivise schemes up to 50MW, and that such schemes will use 90% domestic feedstock.

## Slide 6: Committee on Climate Change Bioenergy report
December 2011 Report from CCC looking at role of bioenergy and sustainability issues:
  Power generation. There should be limited if any support for new large-scale dedicated biomass generation.
    Any longer-term role for new dedicated biomass power plants without CCS should be very limited given its relatively high cost.
    Any near-term investment should be limited to biomass co-firing and the conversion of existing coal-fired power plants.
    While the Government’s current focus on co-firing and conversion is appropriate, safeguards should be introduced to ensure that proposed support for new dedicated biomass under the RO does not result in unnecessary cost escalation or increased emissions.
    For new dedicated biomass power plants, support should be limited to small-scale plants and combined heat and power (CHP) plants, or at a minimum, support for large-scale new dedicated biomass should be limited to a very small number of projects.

## Slide 7: Woodfuel Availability
Source: Woodfuel Demand and Usage in Scotland 2011

## Slide 8: Woodfuel Availability
Source: Woodfuel Demand and Usage in Scotland 2011

## Slide 9: RO Proposals for England & Wales
UK Government describes its approach as “cautious”
Like Scotland it wants to “manage risks associated with long-term locking in of feedstock demand in this sector”
Proposal of 1.5ROCs for dedicated biomass would incentivise plant up to 50MW, with 90% of feedstock coming from domestic sources.
Relevant question would be what would development of 50MW electricity plant mean within Scotland and Scottish wood fuel supplies?

## Slide 10: Modelling woodfuel demand for Scotland
Modelling based on an estimated 6,500odt/13,000 green tonnes wood per MW.
Woodfuel Task Force 2 estimated:
  total resource for 2017/21 @ 5,017,400 odt
  total net available resource for 2017/21 @1.2M odt

## Slide 11: Modelling woodfuel demand for Scotland
 |  | Percentage of 2017/21 overall Scottish resource |  | 
Plant size (MW) | Annual fuel input in odt (single plant) | 1 plant | 5 plants | 10 plants
10 | 65,000 | 1.3 | 6.5 | 13.0
20 | 130,000 | 2.6 | 13.0 | 25.9
50 | 352,000 | 6.5 | 32.4 | 64.8
 |  | Percentage of 2017/21 net available Scottish resource |  | 
Plant size (MW) | Annual fuel input in odt (single plant) | 1 plant | 5 plants | 10 plants
10 | 65,000 | 5.8 | 29.1 | 58.1
20 | 130,000 | 11.6 | 58.1 | 116.2
50 | 352,000 | 29.1 | 145.3 | 290.6

## Slide 12: Relevant wider factors
There remain questions about the scale and pace of development under RHI, but it is clear that demand for wood fibre will be significant.
  3% of Scottish heat = 0.5m odt
Support in England & Wales will have a continued impact on the Scottish market.
Electric plant could act as a stimulant to the market, particularly at local scale as a “first market”.
There may be areas of Scottish woodland not being fully managed or utilised owing to cost and accessibility.

## Slide 13: Recommendations
The Scottish Government would be justified in setting a threshold capacity, both due to greenhouse gas emissions from power generation, and because of constraints on available domestic resource.
While some threshold beneath 50MW can be justified, a level from 50MW down to 20MW would be insufficient (i.e. too high) to limit wider impacts on Scotland’s wood fibre resource.
Our recommendation would be for a 10MW threshold:
  a low deployment of plants (up to 5) would use between approx 30% of net available resource.

## Slide 14: Recommendations (Cont.)
These recommendations are a pragmatic balance between different risks and sector pressures to enable the Scottish Government to best meet a number of different policy objectives highlighted within this report.
The Scottish Government needs to test stakeholder views on assumptions made in this report. In particular:
  What level of deployment is seen as likely
  How much of net available resource different stakeholder groups would be comfortable being used for electricity generation (and therefore not available for use in heat or other markets)
  Likelihood of projects coming forwards below 10MW threshold.

## Slide 15: Report available at: www.forestry.gov.uk/website/forestry.nsf/byunique/infd-8p6eaf
For more information contact
20 December
Maf.smith@xeroenergy.co.uk
2011